## Slide 1: Overview
When CSI40 module is used as 1-Lane or 2-Lane, VIN captures incorrect data.
This bug was caused by the ECO modification of 4Lane highest bit rate input for M3W ES1.0.
  CSI40 Link module violated the interface protocol with VIN.
  So VIN was changed to delay 1 cycle capturing timing to solve above issue because CSI40 Link holds its output 4 bytes data for 1 cycle. However, it was not true when CSI40-Phy used 1- or 2-Lane connection.
  This phenomenon occurs only in M3W(ES1.0 and ES1.1).
CSI40
Link
VIN
In case of 1-Lane connection:
D0[31:24]
D0[23:16]
D0[15:8]
D0[7:0]
D0[31:24]
D0[23:16]
D0[15:8]
D0[31:24]
Shifted 1 byte
Copied MSB
1 byte
In case of 2-Lane connection:
D0[31:24]
D0[23:16]
D0[15:8]
D0[7:0]
D0[31:24]
D0[23:16]
D0[31:24]
Shifted 2 bytes
Copy MSB
2 bytes
D0[23:16]
Expected
32-bits data
Captured
32-bits data
Expected
32-bits data
Captured
32-bits data
1 byte (when 1-Lane connection) or
2 bytes (when 2-Lane connection)
data input
CSI40
Phy
Packed to 4 bytes